## Slide 1
HRI Milipol 2026
Progress Update
Chemical Spill Demo - Ghost Vision 60
STT/TTS Loop, FR on the Move, VLM Testing, DYNO Orchestrator
March 2026
Klass Engineering
Confidential

## Slide 2
ACHIEVEMENT 1
Speech Loop: STT + TTS
1. Push-to-Talk (Operator)
MediaRecorder, WebM/Opus, 250ms chunks
v
2. STT Server (Kognigate :43008)
Whisper ASR, real-time transcripts via WS
v
3. Orchestrator Processing
Transcript -> user_intent -> LLM plan generation
v
4. TTS Server (:8200)
CosyVoice3 Singlish, POST /tts -> WAV
v
5. Dashboard Audio Playback
Base64 WAV -> Audio element auto-play
What's Working
Full bidirectional voice loop
Real-time waveform visualization (mic + TTS)
Transcript history in conversation panel
SPEAK action triggers TTS broadcast
WORKING
Demo Video (SharePoint)
Speech STT + TTS loop demonstration

## Slide 3
ACHIEVEMENT 2
FR on the Move + Dashboard Integration
FR Pipeline (5 FPS)
1
Camera capture (Ghost PC :8889/cam/jpeg)
2
Edge Proxy FR loop (JPEG every 200ms)
3
FR Server (SCRFD + ViT + ByteTrack)
4
Detections broadcast via /fr WebSocket
5
Dashboard overlay (bboxes + identity labels)
Demo Video (SharePoint):
FR on the move + dashboard integration
Dashboard Features
Real-time bounding boxes
Scaled to video display, color-coded: known (teal) vs unknown (orange)
Identity + confidence labels
Name and confidence % displayed above each bbox
FR Temporal Analyzer
10s sliding window, 5s consistency, 60% presence threshold
Orchestrator integration
FR detections sent via /edge WS to FRTemporalAnalyzer for identity confirmation
Auto-reconnect
2s backoff on FR WebSocket disconnect
WORKING

## Slide 4
ACHIEVEMENT 3
VLM Preliminary Testing
VLM Pipeline in DYNO
SCAN_AREA triggered by orchestrator
Frame capture via Edge Proxy (MediaMTX)
JPEG base64 + prompt -> modelapi (OpenAI API)
Analysis returned: hazards, casualties, objects
Replan trigger: keywords or interesting=true
Tested Capabilities
Scene description and object identification
Hazard classification from visual input
Casualty detection and status assessment
Integration with dynamic replanning
WORKING
Model: Qwen3.5-122B-A10B
Demo Scene Use Cases
Scene 1: Office Tables
Detect unconscious workers, assess gas exposure risk
Scene 2: Stacked Boxes
Identify trapped worker, assess structural hazards
Scene 3: Chemical Spill
Locate spill source, identify hazmat containers, detect vapor
Also Supports VERIFY_OBJECT
Same VLM pipeline for targeted object verification
Used in refined plans after SCAN_AREA detects anomalies
Returns structured analysis with class + confidence
Testing Notes (Capacities):
VLM preliminary testing documentation

## Slide 5
ACHIEVEMENT 4
DYNO Orchestrator - Current Progress
DAG-Based Planning (LLM + Verifier)
LLM Planner (Qwen3-Next-80B)
Intent -> JSON plan, retry + temperature escalation
DAG Parser + Schema Validation
Dependency graph, sequential/DAG topology
Symbolic Verifier (6 rules)
Actions, cycles, orphans, battery, safety, depth
Dynamic Replanning
SCAN_AREA replan trigger
Keywords or interesting=true -> cancel + refine + re-execute
4 passing integration tests
Executor + server dynamic replan flow validated
State Machine (7 states)
IDLE -> LISTENING -> PROCESSING
-> AWAITING_CONFIRM -> EXECUTING
-> SPEAKING -> IDLE
Robot Actions (8 total)
CHECK_BATTERY - edge proxy telemetry
NAVIGATE - NavigateToPose (partial waypoint)
SCAN_AREA - frame -> VLM -> analysis + replan
IDENTIFY_PERSON - frame -> FR -> identity
VERIFY_OBJECT - frame -> VLM -> verification
SPEAK / WAIT / ALERT_OPERATOR
Test Coverage: 14 test files
State machine, DAG parser, symbolic verifier
FR/TTS/VLM clients, FR temporal analyzer
Dashboard confirmation, dynamic replanning
Services Integrated
FR Client (WS to :42067), TTS Client (HTTP to :8200)
VLM Client (modelapi chat), Edge Proxy (WS to :8080)
FR Temporal Analyzer (10s window dedup)

## Slide 6
ORCHESTRATOR SHOWCASE
DAG Plans: Initial + Dynamic Replan
Initial Triage Plan (8 steps)
1
CHECK_BATTERY
|
2
NAVIGATE -> Office Area
|
3
SCAN_AREA (people)
|
4
NAVIGATE -> Stacked Boxes
|
5
SCAN_AREA (hazard)
|
6
NAVIGATE -> Spill Source
|
7
SCAN_AREA (hazard)
|
8
SPEAK "Triage complete"
Step 5 SCAN_AREA detected: "chemical, spill, gas"
-> Dynamic replan triggered
Refined Plan (6 steps)
R1
VERIFY_OBJECT (spill source)
|
R2
SCAN_AREA (detailed hazard)
|
R3
SPEAK "Chemical hazard confirmed"
|
R4
NAVIGATE -> Safe perimeter
|
R5
SCAN_AREA (verify perimeter)
|
R6
ALERT_OPERATOR (critical)
Plan ID: triage_plan_001_refined_01

## Slide 7
ROADMAP
Pending Items + Next Steps
Pending Integration Testing
Orchestrator to Navigation testing
End-to-end NAVIGATE action via Edge Proxy to Nav2
VLM integration with Orchestrator
SCAN_AREA + VERIFY_OBJECT live VLM round-trip
STT integration to Dashboard
Push-to-talk mic -> Kognigate STT -> transcript display
STT output to Orchestrator
Transcript stream -> user_intent -> state machine event
Orchestrator TTS output
SPEAK action -> TTS server -> WAV broadcast to dashboard
Recently Completed
Dynamic replan trigger path
SCAN_AREA -> cancel -> refine -> re-execute (4 tests)
VERIFY_OBJECT implemented
Frame -> VLM modelapi -> analysis
Speech STT + TTS loop
Full bidirectional voice with waveform viz
FR on the Move + Dashboard
5 FPS FR pipeline with real-time bbox overlay
VLM scene analysis pipeline
SCAN_AREA -> frame -> VLM -> analysis + replan
Orchestrator core (14 test files)
Planner, executor, state machine, all services
DAG showcase: initial + replan
Triage plan with VERIFY_OBJECT branch