## Slide 1
HRI Milipol 2026
Progress Update
Chemical Spill Demo - Ghost Vision 60
STT/TTS Loop, FR on the Move, VLM Testing, DYNO Orchestrator
March 2026
Klass Engineering
Confidential

## Slide 2
ACHIEVEMENT 1
Speech Loop: STT + TTS
1. Push-to-Talk (Operator)
MediaRecorder, WebM/Opus, 250ms chunks
v
2. STT Server (Kognigate :43008)
Whisper ASR, real-time transcripts via WS
v
3. Orchestrator Processing
Transcript -> user_intent -> LLM plan generation
v
4. TTS Server (:8200)
CosyVoice3 Singlish, POST /tts -> WAV
v
5. Dashboard Audio Playback
Base64 WAV -> Audio element auto-play
What's Working
Full bidirectional voice loop
Real-time waveform visualization (mic + TTS)
Transcript history in conversation panel
SPEAK action triggers TTS broadcast
WORKING
Demo Video (SharePoint)
Speech STT + TTS loop demonstration

## Slide 3
ACHIEVEMENT 2
FR on the Move + Dashboard Integration
FR Pipeline (5 FPS)
1
Camera capture (Ghost PC :8889/cam/jpeg)
2
Edge Proxy FR loop (JPEG every 200ms)
3
FR Server (SCRFD + ViT + ByteTrack)
4
Detections broadcast via /fr WebSocket
5
Dashboard overlay (bboxes + identity labels)
Demo Video (SharePoint):
FR on the move + dashboard integration
Dashboard Features
Real-time bounding boxes
Scaled to video display, color-coded: known (teal) vs unknown (orange)
Identity + confidence labels
Name and confidence % displayed above each bbox
FR Temporal Analyzer
10s sliding window, 5s consistency, 60% presence threshold
Orchestrator integration
FR detections sent via /edge WS to FRTemporalAnalyzer for identity confirmation
Auto-reconnect
2s backoff on FR WebSocket disconnect
WORKING

## Slide 4
ACHIEVEMENT 3
VLM Preliminary Testing
Test Queries (Basic Perception)
Show Basic Perception for context
What brand are the person's shoes?
What objects are on or near the desk in the background?
Is there a second person partially visible in the background?
What text or brand is visible on the person's shirt?
What can be seen through the windows?
Test Summary
Model: Qwen3.5-122B-A10B
Selected for low resource usage + good performance
OpenAI-compatible chat API via modelapi
JPEG base64 + text prompt -> analysis
WORKING
Next Steps for Demo Scenes
Develop endpoints for SCAN_AREA and VERIFY_OBJECT
Create test cases to benchmark SCAN_AREA and VERIFY_OBJECT
Test with different resolutions (camera settings)
Chemical scene testing (3 demo scenes) - PENDING
Integration Path
VLM client uses OpenAI-compatible API
Frame capture -> JPEG base64 -> prompt -> response
SCAN_AREA and VERIFY_OBJECT will share same pipeline
Dynamic replan trigger based on VLM hazard detection
Notes
Demo scene testing (Office/Boxes/Spill) pending
Current tests validate basic perception capability

## Slide 5
ACHIEVEMENT 4
DYNO Orchestrator: LLM Prompting
User Prompt
Simple natural language input
"can u investigate"
↓
System Prompt
Role + Rules
Robotic DAG planner, strict JSON output
Allowed Actions (8)
CHECK_BATTERY, NAVIGATE, SCAN_AREA, VERIFY_OBJECT, IDENTIFY_PERSON, SPEAK, ALERT_OPERATOR, WAIT
Map
lobby -> office_tables -> stacked_boxes -> spill_source
Rules
CHECK_BATTERY before NAVIGATE, DAG with branch/merge, SCAN_AREA at locations, suspicious -> VERIFY_OBJECT + IDENTIFY_PERSON
LLM Output - 12-Step DAG Plan
Inferred Intent
"Investigate facility for anomalies and security threats."
Plan ID
INV-2023-001 (DAG topology)
Execution Flow
1:CHECK_BATTERY -> 2:NAVIGATE(lobby) -> 3:SCAN_AREA -> 4:NAVIGATE(office_tables) -> 5:SCAN_AREA
Parallel Branch (after step 5)
6:VERIFY_OBJECT
7:IDENTIFY_PERSON
Merge -> Continue
Both 6+7 complete -> 8:NAVIGATE(stacked_boxes) -> 9:NAVIGATE(spill_source) -> 10:SCAN_AREA -> 11:SPEAK -> 12:ALERT_OPERATOR
Model: Qwen3-Next-80B (modelapi.klass.dev)

## Slide 6
ORCHESTRATOR SHOWCASE
DAG Plan: "Investigate facility"
LLM generates 12-step DAG with parallel investigation branch
Sequential Path (Steps 1-5)
1
CHECK_BATTERY
|
2
NAVIGATE -> lobby
|
3
SCAN_AREA (lobby)
|
4
NAVIGATE -> office_tables
|
5
SCAN_AREA (office_tables)
PARALLEL BRANCH (both depend on step 5)
6
VERIFY_OBJECT
7
IDENTIFY_PERSON
|\ (merge)
Sequential Path (Steps 8-12)
8
NAVIGATE -> stacked_boxes
|
9
NAVIGATE -> spill_source
|
10
SCAN_AREA (spill_source)
|
11
SPEAK "Investigation complete"
|
12
ALERT_OPERATOR
Plan ID: INV-2023-001 | Topology: DAG | 12 steps
Step 8 waits for BOTH step 6 AND step 7 to complete (merge point)

## Slide 7
ROADMAP
Pending Items + Next Steps
Pending Integration Testing
Orchestrator to Navigation testing
End-to-end NAVIGATE action via Edge Proxy to Nav2
VLM integration with Orchestrator
SCAN_AREA + VERIFY_OBJECT live VLM round-trip
STT integration to Dashboard
Push-to-talk mic -> Kognigate STT -> transcript display
STT output to Orchestrator
Transcript stream -> user_intent -> state machine event
Orchestrator TTS output
SPEAK action -> TTS server -> WAV broadcast to dashboard
Recently Completed
Dynamic replan trigger path
SCAN_AREA -> cancel -> refine -> re-execute (4 tests)
VERIFY_OBJECT implemented
Frame -> VLM modelapi -> analysis
Speech STT + TTS loop
Full bidirectional voice with waveform viz
FR on the Move + Dashboard
5 FPS FR pipeline with real-time bbox overlay
VLM scene analysis pipeline
SCAN_AREA -> frame -> VLM -> analysis + replan
Orchestrator core (14 test files)
Planner, executor, state machine, all services
DAG showcase: initial + replan
Triage plan with VERIFY_OBJECT branch